FINALTERM  EXAMINATION

Spring 2010

CS401- Computer Architecture and Assembly Language Programming (Session - 2)

Time: 90 min

Marks: 58

| For Teacher's Use Only |
| --- |
| Q No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | Total |
| Marks |  |  |  |  |  |  |  |  |  |
| Q No. | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 |  |
| Marks |  |  |  |  |  |  |  |  |  |
| Q No. | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 |  |
| Marks |  |  |  |  |  |  |  |  |  |
| Q No. | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 |  |
| Marks |  |  |  |  |  |  |  |  |  |
| Q No. | 33 | 34 | 35 | 36 |  |  |  |  |  |
| Marks |  |  |  |  |  |  |  |  |  |

Question No: 1    ( Marks: 1 )    - Please choose one

Suppose AL contains 5 decimal then after two left shifts produces the value as

► 5

► 10

► 15

► 20

Question No: 2    ( Marks: 1 )    - Please choose one

In graphics mode a location in video memory corresponds to a _____________ on the screen.

► line

► dot

► circle

► rectangle

Question No: 3    ( Marks: 1 )    - Please choose one

Creation of threads can be

► static

► dynamic

► easy

► difficult

Question No: 4    ( Marks: 1 )    - Please choose one

The thread registration code initializes the PCB and adds it to the linked list so that the __________ will give it a turn.

► assembler

► scheduler

► linker

► debugger

Question No: 5    ( Marks: 1 )    - Please choose one

VESA VBE 2.0 is a standard for

► High resolution Mode

► Low resolution Mode

► Medium resolution Mode

► Very High resolution Mode

Question No: 6    ( Marks: 1 )    - Please choose one

Which of the following gives the more logical view of the storage medium

► BIOS

► DOS

► Both

► None

Question No: 7    ( Marks: 1 )    - Please choose one

Which of the following IRQs is derived by a key board?

► IRQ 0

► IRQ 1

► IRQ 2

► IRQ 3

Question No: 8    ( Marks: 1 )    - Please choose one

Which of the following IRQs is used for Floppy disk derive?

► IRQ 4

► IRQ 5

► IRQ 6

► IRQ 7

Question No: 9    ( Marks: 1 )    - Please choose one

Which of the following pins of a parallel port connector are grounded?

► 10-18

► 18-25

► 25-32

► 32-39

Question No: 10    ( Marks: 1 )    - Please choose one

The physical address of IDT( Interrupt Descriptor Table) is stored in _______

► GDTR

► IDTR

► IVT

► IDTT

Question No: 11    ( Marks: 1 )    - Please choose one

In NASM an imported symbol  is declared with the ............................ while and exported symbol is declared with the ............................

► Global directive, External directive

► External directive, Global directive

► Home Directive, Foreign Directive

► Foreign Directive, Home Directive

Question No: 12    ( Marks: 1 )    - Please choose one

In 68K processors there is a ........................ program counter (PC) that holds the address of currently executing instruction

► 8bit

► 16bit

► 32bit

► 64bit

Question No: 13    ( Marks: 1 )    - Please choose one

To reserve 8-bits in memory ___ directive is used.

► db

► dw

► dn

► dd

Question No: 14    ( Marks: 1 )    - Please choose one

In the “mov ax, 5”     5 is the __________ operand.

► source

► destination

► memory

► register

Question No: 15    ( Marks: 1 )    - Please choose one

RETF will pop the segment address in the

► CS register

► DS register

► SS register

► ES register

Question No: 16    ( Marks: 1 )    - Please choose one

For the execution of the instruction “DIV  BL”, the implied dividend will be stored in

► AX

► BX

► CX

► DX

Question No: 17    ( Marks: 1 )    - Please choose one

When a number is divided by zero ”A Division by 0” interrupt is generated. Which instruction is used for this purpose

► INT 0

► INT 1

► INT 2

► This interrupt is generated automatically

Question No: 18    ( Marks: 1 )    - Please choose one

INT 21 service 01H is used to read character from standard input with echo. It returns the result in  ______ register.

► AL

► BL

► CL

► BH

Question No: 19    ( Marks: 1 )    - Please choose one

BIOS sees the disks as

► logical storage

► raw storage

► in the form of sectors only

► in the form of tracks only

Question No: 20    ( Marks: 1 )    - Please choose one

In 9pin DB 9, which pin number is assigned to CD (Carrier Detect) ?

► 1

► 2

► 3

► 4

Question No: 21    ( Marks: 1 )    - Please choose one

In 9pin DB 9, Signal ground is assigned on pin number

► 4

► 5

► 6

► 3

Question No: 22    ( Marks: 1 )    - Please choose one

In 9pin DB 9, RI (Ring Indicator) is assigned on pin number

► 6

► 7

► 8

► 9

Question No: 23    ( Marks: 1 )    - Please choose one

Motorola 68K processors have ....................... 23bit general purpose registers.

► 4

► 8

► 16

► 32

Question No: 24    ( Marks: 1 )    - Please choose one

When two devices in the system want to use the same IRQ line then what will happen?

► An IRQ Collision

► An IRQ Conflict

► An IRQ Crash

► An IRQ Blockage

Question No: 25    ( Marks: 1 )    - Please choose one

In the instruction  MOV AX, 5 the number of operands are

► 1

► 2

► 3

► 4

Question No: 26    ( Marks: 1 )    - Please choose one

Which flags are NOT used for mathematical operations ?

► Carry, Interrupt and Trap flag.

► Direction, Interrupt and Trap flag.

► Direction, Overflow and Trap flag.

► Direction, Interrupt and Sign flag.

Question No: 27    ( Marks: 2 )

How can we improve the speed of multitasking?

Ans:

We can improve the speed of multitasking by changing the frequency of timer interrupt.

Question No: 28    ( Marks: 2 )

Write instructions to do the following. Copy contents of memory location with offset 0025 in the current data segment into AX.

Ans:

Mov ax , [0025]

mov[0fff], ax

mov  ax , [0010]

mov [002f] , ax

Question No: 29    ( Marks: 2 )

Write types of Devices?

Ans:

There are two types devices used  in pc.

- Input devices(keyboard, mouse,)

- Output devices.(monitor, printer)

Question No: 30    ( Marks: 2 )

What dose descriptor 1st 16 bit tell?

Ans:

Each segment is describe by the descriptor like

- base,

- limit,

- and attributes,

it  basically define the actual base address.

Question No: 31    ( Marks: 3 )

List down any three common video services for INT 10 used in text mode.

Ans:

INT 10 - VIDEO - SET TEXT-MODE CURSOR SHAPE

AH = 01h

CH = cursor start and options

CL = bottom scan line containing cursor (bits 0-4)

Question No: 32    ( Marks: 3 )

How to create or Truncate File using INT 21 Service?

Ans:

INT 21 - TRUNCATE FILE

AH = 3Ch

CX = file attributes

DS:DX -> cs401 filename

Return:

CF = error flag

AX = file handle or error code

Question No: 33    ( Marks: 3 )

How many Types of granularity also name them?

Ans:

There are three types of granuality :

- Data Granularity

- Business Value Granularity

- Functionality Granularity

Question No: 34    ( Marks: 5 )

How to read disk sector into memory using INT 13 service?

Ans:

INT 13 - DISK - READ SECTOR(S) INTO MEMORY :

AH = 02h

AL = number of sectors to read (must be nonzero)

CH = low eight bits of cylinder number

CL = 		sector number 1-63 (bits 0-5)

high two bits of cylinder (bits 6-7, hard disk only)

DH = head number

DL = drive number (bit 7 set for hard disk)

ES:BX -> data buffer

Return:

CF = error flag

AH = error code

AL = number of sectors transferred

Question No: 35    ( Marks: 5 )

The program given below is written in assembly language. Write a program in C to call this assembly routine.

[section .text]

global        swap

swap:        mov  ecx,[esp+4]      ; copy parameter p1 to ecx

mov  edx,[esp+8]      ; copy parameter p2 to edx

mov  eax,[ecx]           ; copy *p1 into eax

xchg eax,[edx]           ; exchange eax with *p2

mov  [ecx],eax           ; copy eax into *p1

ret                               ; return from this function

Ans:

The above code will assemble in c through this command. Other aurwise error will occur.

Nasm-f win32 swap .asm

This command will generate swap.obj file.

The code for given program will be as follow.

#include <stdio.h>

Void swap(int* pl, int* p2);

Int main()

{

Int a=10,

Int b= 20;

Print f (“a=%d b=%d\n” , a ,b);

Swap (&a ,&b);

Print f (“a=%d b=%d\n” , a ,b);

System ( “pause”);

Return 0;

}

Question No: 36    ( Marks: 5 )

Write the code of “break point interrupt routine”.

Ans:

Breakpoint interrupts service routine :

debugISR:	  push bp

mov  bp, sp             ; …………….to read cs, ip and flags

push ax

push bx

push cx

push dx

push si

push di

push ds

push es

sti                     ;…………………….. waiting for keyboard interrupt

push cs

pop  ds                 ;…………………… initialize ds to data segment

mov  ax, [bp+4]

mov  es, ax             ; ………………….load interrupted segment in es

dec  word [bp+2]        ; ……………….decrement the return address

mov  di, [bp+2]         ;………………… read the return address in di

mov  word [opcodepos], di ;…………. remember the return position

mov  al, [opcode]       ; …………..load the original opcode

mov  [es:di], al        ;………….. restore original opcode there

mov  byte [flag], 0     ; …………set flag to wait for key

call clrscr             ;……………. clear the screen

mov  si, 6              ; …………..first register is at bp+6

mov  cx, 12             ;………… total 12 registers to print

mov  ax, 0              ; …………..start from row 0

mov  bx, 5              ; ………….print at column 5

push ax                 ; ………………..row number

push bx                 ;………………. column number

mov  dx, [bp+si]

push dx                 ;………………. number to be printed

call printnum           ;…………….. print the number

sub  si, 2              ; ……………….point to next register

inc  ax                 ; ………………..next row number

loop l3                 ; ……………….repeat for the 12 registers

mov  ax, 0              ; ………………..start from row 0

mov  bx, 0              ; ………………..start from column 0

mov  cx, 12             ; …………………..total 12 register names

mov  si, 4              ;……………………. each name length is 4 chars

mov  dx, names          ; …………………..offset of first name in dx

push ax                 ;………………………. row number

push bx                 ; ………………………column number

push dx                 ; ……………………….offset of string

push si                 ; ………………………….length of string

call printstr           ; ………………………….print the string

add  dx, 4              ;………………………….. point to start of next string

inc  ax                 ; ……………………………new row number

loop l1                 ;…………………………….. repeat for 12 register names

or word [bp+6], 0x0100  ; ……………………set TF in flags image on stack

keywait:      cmp  byte [flag], 0     ;……………………. has a key been pressed

je   keywait            ;            ………………….. no, check again

pop es

pop ds

pop di

pop si

pop dx

pop cx

pop bx

pop ax

pop bp

iret

start:        xor  ax, ax

mov  es, ax             ;            ……………………point es to IVT base

mov  word [es:1*4], trapisr ;…………………. store offset at n*4

mov  [es:1*4+2], cs     ;      …………………...store segment at n*4+2

mov  word [es:3*4],            …………………..debugisr ; store offset at n*4

mov  [es:3*4+2], cs     ;      …………………..store segment at n*4+2

cli                     ;                  ………………….disable interrupts

mov  word [es:9*4], kbisr ; ………………….store offset at n*4

mov  [es:9*4+2], cs     ; ……………………...store segment at n*4+2

sti                     ;             ………………………enable interrupts